## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 10 – Complex Pipelines, Out-of-Order Issue, Register Renaming
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last time in Lecture 9
Modern page-based virtual memory systems provide:
  Translation, Protection, Virtual memory.
Translation and protection information stored in page tables, held in main memory
Translation and protection information cached in “translation-lookaside buffer” (TLB) to provide single-cycle translation+protection check in common case
Virtual memory interacts with cache design
  Physical cache tags require address translation before tag lookup, or use untranslated offset bits to index cache.
  Virtual tags do not require translation before cache hit/miss determination, but need to be flushed or extended with ASID to cope with context swaps. Also, must deal with virtual address aliases (usually by disallowing copies in cache).

## Slide 3: Complex Pipelining: Motivation
Pipelining becomes complex when we want high performance in the presence of:
Long latency or partially pipelined floating-point units
Memory systems with variable access time
Multiple arithmetic and memory units

## Slide 4: Issues in Complex Pipeline Control
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPRs
FPRs
Structural conflicts at the execution stage if some FPU or memory unit is not pipelined and takes more than one cycle
Structural conflicts at the write-back stage due to variable latencies of different functional units
Out-of-order write hazards due to variable latencies of different functional units
How to handle exceptions?

## Slide 5: Recap: Complex In-Order Pipeline
Delay writeback so all operations have same latency to W stage
  Write ports never oversubscribed (one inst. in & one inst. out every cycle)
  Stall pipeline on long latency operations, e.g., divides, cache misses
  Handle exceptions in-order at commit point
Commit Point
PC
Inst. Mem
D
Decode
X1
X2
Data Mem
W
+
GPRs
X2
W
FAdd
X3
X3
FPRs
X1
X2
FMul
X3
X2
FDiv
X3
Unpipelined divider
How to prevent increased writeback latency from slowing down single-cycle integer operations?
Bypassing

## Slide 6: Complex Pipeline
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPR’s
FPR’s
Can we solve write hazards without equalizing all pipeline depths and without bypassing?

## Slide 7: Types of Data Hazards
Consider executing a sequence of
rk ← ri op rj
type of instructions
Data-dependence
      r3 ← r1 op r2 Read-after-Write
      r5 ← r3 op r4 (RAW) hazard
Anti-dependence
      r3 ← r1 op r2 Write-after-Read
      r1 ← r4 op r5 (WAR) hazard
Output-dependence
      r3 ← r1 op r2 Write-after-Write
      r3 ← r6 op r7 (WAW) hazard

## Slide 8: Register vs. Memory Dependence
Data hazards due to register operands can be determined at the decode stage, but data hazards due to memory operands can be determined only after computing the effective address
Store: M[r1 + disp1] ← r2
Load: r3 ← M[r4 + disp2]
Does (r1 + disp1) = (r4 + disp2) ?

## Slide 9: Data Hazards: An Example
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
RAW Hazards
WAR Hazards
WAW Hazards

## Slide 10: Instruction Scheduling
I6
I2
I4
I1
I5
I3
Valid orderings:
in-order I1 I2 I3 I4 I5 I6
out-of-order
out-of-order
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMULT.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
I2 I1 I3 I4 I5 I6
I1 I2 I3 I5 I4 I6

## Slide 11: Out-of-order Completion In-order Issue
Latency
I1 FDIV.D f6, f6, f4 4
I2 FLD f2, 45(x3) 1
I3 FMULT.D f0, f2, f4 3
I4 FDIV.D f8, f6, f2 4
I5 FSUB.D f10, f0, f6 1
I6 FADD.D f6, f8, f2 1
in-order comp 1 2
out-of-order comp 1 2
1 2 3 4 3 5 4 6 5 6
2 3 1 4 3 5 5 4 6 6

## Slide 12: When is it Safe to Issue an Instruction?
Suppose a data structure keeps track of all the instructions in all the functional units
The following checks need to be made before the Issue stage can issue an instruction into execution
Is the required function unit available?
Is the input data available? (RAW?)
Is it safe to write the destination? (WAR?WAW?)
Is there a structural conflict at the WB stage?

## Slide 13: A Data Structure for Correct Issue Keeps track of the status of Functional Units
The instruction i at the Issue stage consults this table
  FU available? check the busy column
  RAW? search the dest column for i’s sources
  WAR? search the source columns for i’s destination
  WAW? search the dest column for i’s destination
An entry is added to the table if no hazard is detected;
An entry is removed from the table after Write-Back
Name Busy Op Dest Src1 Src2
  Int
  Mem
  Add1
  Add2
  Add3
  Mult1
  Mult2
  Div

## Slide 14: Simplifying the Data Structure Assuming In-order Issue
Suppose the instruction is not issued by the Issue stage if a RAW hazard exists or the required FU is busy, and that operands are registered by functional unit on issue:
  Can the issued instruction cause a
    WAR hazard ?
    WAW hazard ?
NO: Earlier instructions read their operands at issue
YES: Out-of-order completion
Notes:   Can the dispatched instruction cause a
    WAR hazard ? NO: Operands read at issue
    WAW hazard ? YES: Out-of-order completion

## Slide 15: Simplifying the Data Structure ...
No WAR hazard
   no need to keep src1 and src2
The Issue stage does not issue an instruction in case of a WAW hazard
   a register name can occur at most once in the dest column
WP[reg#] : a bit-vector to record the registers for which writes are pending
  These bits are set by the Issue stage and cleared by the WB stage
   Each pipeline stage in the FU's must carry the register destination field and a flag to indicate if it is valid

## Slide 16: Scoreboard for In-order Issue
Busy[FU#] : a bit-vector to indicate FU’s availability.
        (FU = Int, Add, Mult, Div)
  These bits are hardwired to FU's.
WP[reg#] : a bit-vector to record the registers for which writes are pending.
  These bits are set by Issue stage and cleared by WB stage
Issue checks the instruction (opcode dest src1 src2)
against the scoreboard (Busy & WP) before issue
    FU available?
    RAW?
    WAR?
    WAW?
Busy[FU#]
WP[src1] or WP[src2]
cannot arise
WP[dest]

## Slide 17: Scoreboard Dynamics
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMULT.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
  Functional Unit Status Registers Reserved
  Int(1) Add(1) Mult(3) Div(4) WB for Writes
t0 I1 f6 f6
t1 I2 f2 f6 f6, f2
t2 f6 f2 f6, f2 I2
t3 I3 f0 f6 f6, f0
t4 f0 f6 f6, f0 I1
t5 I4 f0 f8 f0, f8
t6 f8 f0 f0, f8 I3
t7 I5 f10 f8 f8, f10
t8 f8 f10 f8, f10 I5
t9 f8 f8 I4
t10 I6 f6 f6
t11 f6 f6 I6

## Slide 18: In-Order Issue Limitations: an example
latency
1 FLD f2, 34(x2) 1
2 FLD f4, 45(x3) long
3 FMULT.D f6, f4, f2 3
4 FSUB.D f8, f2, f2 1
5 FDIV.D f4, f2, f8 4
6 FADD.D f10, f6, f4 1
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
1
2
3
4
5
6
In-order issue restriction prevents instruction 4 from being issued

## Slide 19: Out-of-Order Issue
Issue stage buffer holds multiple instructions waiting to issue.
Decode adds next instruction to buffer if there is space and the instruction does not cause a WAR or WAW hazard.
  Note: WAR possible again because issue is out-of-order (WAR not possible with in-order issue and registering of input operands at functional unit)
Any instruction in buffer whose RAW hazards are satisfied can be issued (for now, at most one issue per cycle). On a write back (WB), new instructions may get enabled.
IF
ID
WB
ALU
Mem
Fadd
Fmul
Issue

## Slide 20: Issue Limitations: In-Order and Out-of-Order
latency
1 FLD f2, 34(x2) 1
2 FLD f4, 45(x3) long
3 FMULT.D f6, f4, f2 3
4 FSUB.D f8, f2, f2 1
5 FDIV.D f4, f2, f8 4
6 FADD.D f10, f6, f4 1
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
1
2
3
4
5
6
Out-of-order: 1 (2,1) 4 4 . . . . 2 3 . . 3 5 . . . 5 6 6
Out-of-order execution did not allow any significant improvement!

## Slide 21: How many instructions can be in the pipeline?
Which features of an ISA limit the number of
instructions in the pipeline?
Out-of-order issue by itself does not provide any significant performance improvement!
Number of Registers
Notes: Ilustrates how one feature alone may not help – happens today when people study single new idea in a very detailed model.

## Slide 22: CS152 Administrivia
Midterm in class time slot Monday March 1
  Covers lectures 1 – 9, plus assigned problem sets, labs, book readings
  Excludes this lecture
Zoom proctoring via individual breakout rooms
  Can use 1-page cheat sheat, but otherwise no external help
  Dry run in section on Friday
Lab 2 due Monday March 8

## Slide 23: CS252 Administrivia
Project Proposal due tonight
Proposal should be one page PDF including:
  Title
  Team member names
  What are you trying to do?
  How is it done today?
  What is your idea for improvement and why do you think you’ll be successful
  What infrastructure are you going to use for your project?
  Project timeline with milestones
Mail PDF of proposal to instructors
Give ~5-minute presentations in class in discussion section time on Thursday March 4th and March 11th

## Slide 24: Overcoming the Lack of Register Names
Floating-point pipelines often cannot be kept filled with small number of registers.
IBM 360 had only 4 floating-point registers
Can a microarchitecture use more registers than
specified by the ISA without loss of ISA compatibility ?
    Robert Tomasulo of IBM suggested an ingenious solution in 1967 using on-the-fly register renaming

## Slide 25: Issue Limitations: In-Order and Out-of-Order
latency
1 FLD f2, 34(x2) 1
2 FLD f4, 45(x3) long
3 FMULT.D f6, f4, f2 3
4 FSUB.D f8, f2, f2 1
5 FDIV.D f4’, f2, f8 4
6 FADD.D f10, f6, f4’ 1
1
2
3
4
5
6
Any antidependence can be eliminated by renaming.
    (renaming  additional storage)
    Can it be done in hardware?
yes!
X
In-order: 1 (2,1) . . . . . . 2 3 4 4 3 5 . . . 5 6 6
Out-of-order: 1 (2,1) 4 4 5 . . . 2 (3,5) 3 6 6

## Slide 26: Register Renaming
Decode does register renaming and adds instructions to the issue-stage instruction reorder buffer (ROB)
 renaming makes WAR or WAW hazards impossible
Any instruction in ROB whose RAW hazards have been satisfied can be issued
 Out-of-order or dataflow execution
IF
ID
WB
ALU
Mem
Fadd
Fmul
Issue

## Slide 27: Renaming Structures
Renaming
table &
regfile
Reorder
buffer
Load
Unit
FU
FU
Store
Unit
< t, result >
Ins# use exec op p1 src1 p2 src2
t1
t2
.
.
tn
Instruction template (i.e., tag t) is allocated by the Decode stage, which also associates tag with register in regfile
When an instruction completes, its tag is deallocated
Replacing the
tag by its value
is an expensive
operation

## Slide 28: Reorder Buffer Management
Instruction slot is candidate for execution when:
  It holds a valid instruction (“use” bit is set)
  It has not already started execution (“exec” bit is clear)
  Both operands are available (p1 and p2 are set)
t1
t2
.
.
.
tn
ptr2
next to
deallocate
ptr1
next
available
Ins# use exec op p1 src1 p2 src2
Destination registers are renamed to the instruction’s slot tag
ROB managed circularly
  “exec” bit is set when instruction begins execution
  When an instruction completes its “use” bit is marked free
  ptr2 is incremented only if the “use” bit is marked free

## Slide 29: Renaming & Out-of-order Issue An example
When are tags in sources
replaced by data?
When can a name be reused?
1 FLD f2, 34(x2)
2 FLD f4, 45(x3)
3 FMULT.D f6, f4, f2
4 FSUB.D f8, f2, f2
5 FDIV.D f4, f2, f8
6 FADD.D f10, f6, f4
Renaming table
Reorder buffer
Ins# use exec op p1 src1 p2 src2
t1
t2
t3
t4
t5
.
.
data / ti
p data
f1
f2
f3
f4
f5
f6
f7
f8
Whenever an FU produces data
Whenever an instruction completes
t1
1 1 0 LD
t2
2 1 0 LD
5 1 0 DIV 1 v1 0 t4
4 1 0 SUB 1 v1 1 v1
t4
3 1 0 MUL 0 t2 1 v1
t3
t5
v1
v1
1 1 1 LD
0
4 1 1 SUB 1 v1 1 v1
4 0
v4
5 1 0 DIV 1 v1 1 v4
2 1 1 LD
2 0
3 1 0 MUL 1 v2 1 v1

## Slide 30: IBM 360/91 Floating-Point Unit R. M. Tomasulo, 1967
Mult
1
1
2
3
4
5
6
load
buffers
(from
memory)
1
2
3
4
Adder
1
2
3
Floating-Point
Regfile
store buffers
(to memory)
...
instructions
Common bus ensures that data is made available immediately to all the instructions waiting for it.
Match tag, if equal, copy value & set presence “p”.
Distribute
instruction
templates
by
functional
units
< tag, result >
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
2
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data

## Slide 31: IBM ACS
Second supercomputer project (Y) started at IBM in response to CDC6600
Multiple Dynamic instruction Scheduling (DIS) invented by Lynn Conway for ACS
  Used unary encoding of register specifiers and wired-OR logic to detect any hazards (similar design used in Alpha 21264 in 1995!)
Seven-issue, out-of-order processor
  Two decoupled streams, each with DIS
Cancelled in favor of IBM360-compatible machines

## Slide 32: Out-of-Order Fades into Background
Out-of-order processing implemented commercially in 1960s, but disappeared again until 1990s as two major problems had to be solved:
Precise traps
  Imprecise traps complicate debugging and OS code
  Note, precise interrupts are relatively easy to provide
Branch prediction
  Amount of exploitable instruction-level parallelism (ILP) limited by control hazards
Also, simpler machine designs in new technology beat complicated machines in old technology
  Big advantage to fit processor & caches on one chip
  Microprocessors had era of 1%/week performance scaling

## Slide 33: In-Order Commit for Precise Traps
In-order instruction fetch and decode, and dispatch to reservation stations inside reorder buffer
Instructions issue from reservation stations out-of-order
Out-of-order completion, values stored in temporary buffers
Commit is in-order, checks for traps, and if none updates architectural state
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Trap?
Kill
Kill
Kill
Inject handler PC

## Slide 34: Separating Completion from Commit
Re-order buffer holds register results from completion until commit
  Entries allocated in program order during decode
  Buffers completed values and exception state until in-order commit point
  Completed values can be used by dependents before committed (bypassing)
  Each entry holds program counter, instruction type, destination register specifier and value if any, and exception status (info often compressed to save hardware)
Memory reordering needs special data structures
  Speculative store address and data buffers
  Speculative load address and data buffers

## Slide 35: Phases of Instruction Execution
Fetch: Instruction bits retrieved from instruction cache.
I-cache
Fetch Buffer
Issue Buffer
Functional Units
Architectural
State
Execute: Instructions and operands issued to functional units. When execution completes, all results and exception flags are available.
Decode: Instructions dispatched to appropriate issue buffer.
Result Buffer
Commit: Instruction irrevocably updates architectural state (aka “graduation” or “retirement” ), or takes precise trap.
PC
Commit
Decode/Rename

## Slide 36: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)