## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 11 – Out-of-Order Execution
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 10
Pipelining is complicated by multiple and/or variable latency functional units
Out-of-order and/or pipelined execution requires tracking of dependencies (RAW, WAR, WAW)
OoO issue limited by WAR and WAW hazards caused by reuse of architectural register names, removed by register renaming
OoO issue and register renaming invented in mid-1960s but disappeared in practice until 1990s, as simpler architecture approaches (pipelining, caches) could more easily take advantage of technology scaling
Also, two important problems had to be solved:
  Control hazards
  Precise traps and interrupts

## Slide 3: Recap: In-Order Commit for Precise Traps
In-order instruction fetch and decode, and dispatch to reservation stations inside reorder buffer
Instructions issue from reservation stations out-of-order
Out-of-order completion, values stored in temporary buffers
Commit is in-order, checks for traps, and if none updates architectural state
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Trap?
Kill
Kill
Kill
Inject handler PC

## Slide 4: Phases of Instruction Execution
Fetch: Instruction bits retrieved from instruction cache.
I-cache
Fetch Buffer
Issue Buffer
Functional Units
Architectural
State
Execute: Instructions and operands issued to functional units. When execution completes, all results and exception flags are available.
Decode: Instructions dispatched to appropriate issue buffer.
Result Buffer
Commit: Instruction irrevocably updates architectural state (aka “graduation” or “retirement” ), or takes precise trap.
PC
Commit
Decode/Rename

## Slide 5: In-Order versus Out-of-Order Phases
Instruction fetch/decode/rename always in-order
  Need to parse ISA sequentially to get correct semantics
  CS252:Proposals for speculative OoO instruction fetch, e.g., Multiscalar. Predict control flow and data dependencies across sequential program segments fetched/decoded/executed in parallel, fixup if prediction wrong
Dispatch (place instruction into machine buffers to wait for issue) also always in-order
  Some use “Dispatch” to mean “Issue”, but not in these lectures

## Slide 6: In-Order Versus Out-of-Order Issue
In-order (InO) issue:
  Issue stalls on RAW dependencies or structural hazards, or possibly WAR/WAW hazards
  Instruction cannot issue to execution units unless all preceding instructions have issued to execution units
Out-of-order (OoO) issue:
  Instructions dispatched in program order to reservation stations (or other forms of instruction buffer) to wait for operands to arrive, or other hazards to clear
  While earlier instructions wait in issue buffers, following instructions can be dispatched and issued out-of-order

## Slide 7: In-Order versus Out-of-Order Completion
All but simplest machines have out-of-order completion, due to different latencies of functional units and desire to bypass values as soon as available
Classic RISC 5-stage integer pipeline just barely has in-order completion
  Load takes two cycles, but following one-cycle integer op completes at same time, not earlier
  Adding pipelined FPU immediately brings OoO completion

## Slide 8: In-Order versus Out-of-Order Commit
In-order commit supports precise traps, standard today
  CS252: Some proposals to reduce the cost of in-order commit by retiring some instructions early to compact reorder buffer, but this is just an optimized in-order commit
Out-of-order commit was effectively what early OoO machines implemented (imprecise traps) as completion irrevocably changed machine state
  i.e., complete == commit in these machines

## Slide 9: OoO Design Choices
Where are reservation stations?
  Part of reorder buffer, or in separate issue window?
  Distributed by functional units, or centralized?
How is register renaming performed?
  Tags and data held in reservation stations, with separate architectural register file
  Tags only in reservation stations, data held in unified physical register file

## Slide 10: “Data-in-ROB” Design (HP PA8000, Pentium Pro, Core2Duo, Nehalem)
Managed as circular buffer in program order, new instructions dispatched to free slots, oldest instruction committed/reclaimed when done (“p” bit set on result)
Tag is given by index in ROB (Free pointer value)
In dispatch, non-busy source operands read from architectural register file and copied to Src1 and Src2 with presence bit “p” set. Busy operands copy tag of producer and clear “p” bit.
Set valid bit “v” on dispatch, set issued bit “i” on issue
On completion, search source tags, set “p” bit and copy data into src on tag match. Write result and exception flags to ROB.
On commit, check exception status, and copy result into architectural register file if no trap.
On trap, flush machine and ROB, set free=oldest, jump to handler
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Oldest
Free

## Slide 11: Managing Rename for Data-in-ROB
If “p” bit set, then use value in architectural register file
Else, tag field indicates instruction that will/has produced value
For dispatch, read source operands <p,tag,value> from arch. regfile, then also read <p,result> from producing instruction in ROB at tag index, bypassing as needed. Copy operands to ROB.
Write destination arch. register entry with <0,Free,_>, to assign tag to ROB index of this instruction
On commit, update arch. regfile with <1,_,Result> if tag matches, otherwise update with <0,_,Result>. (Tag value is not updated)
On trap, reset table (All p=1)
Tag
p
Value
Tag
p
Value
Tag
p
Value
Tag
p
Value
One entry per arch. register
Rename table associated with architectural registers, managed in decode/dispatch

## Slide 12: Data Movement in Data-in-ROB Design
ROB
Architectural Register File
Read operands during decode
Read operands at issue
Functional Units
Read results for commit
Bypass newer values at dispatch
Result Data
Write results at completion
Write results at commit
Source Operands
Write sources in dispatch

## Slide 13: CS152 Administrivia
PS 3 out today, due Monday March 16
Lab 2 due Monday March 8
  Lab 2 takes time to run, so please get started ASAP
  Don’t wait till Sunday!
  Can share directed simulation results but must do own analysis.
  Look at pinned README on Piazza
Midterms being graded, within a week
  Regrade requests up to one week after exams returned
Please respond to survey of midterm technical issues
  This is tied to your email address
Please also respond to course progress survey
  Please give feedback on course so far
  This survey is anonymous

## Slide 14: CS252 Administrivia
Project proposal presentations March 4 (tomorrow) in discussion section
  10-minute per project including Q&A with rest of class
  Schedule on Piazza

## Slide 15: Unified Physical Register File (MIPS R10K, Alpha 21264, Intel Pentium 4 & Sandy/Ivy Bridge)
Rename all architectural registers into a single physical register file during decode, no register values read
Functional units read and write from single unified register file holding committed and temporary registers in execute
Commit only updates mapping of architectural register to physical register, no data movement
Unified Physical Register File
Read operands at issue
Functional Units
Write results at completion
Committed Register Mapping
Decode Stage Register Mapping

## Slide 16: Lifetime of Physical Registers
ld x1, (x3)
addi x3, x1, #4
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x11)
ld P1, (Px)
addi P2, P1, #4
sub P3, Py, Pz
add P4, P2, P3
ld P5, (P1)
add P6, P5, P4
sd P6, (P1)
ld P7, (Pw)
Rename
When can we reuse a physical register?
When next writer of same architectural register commits
Physical regfile holds committed and speculative values
Physical registers decoupled from ROB entries (no data in ROB)

## Slide 17: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
ROB
Rename Table
Physical Regs
Free List
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
p
p
p
P0
P1
P3
P2
P4
(LPRd requires third read port on Rename Table for each instruction)
<x1>
P8
p

## Slide 18: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8

## Slide 19: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1

## Slide 20: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3

## Slide 21: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2

## Slide 22: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4

## Slide 23: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 x1 P0
x addi P0 x3 P1
x sub p P6 p P5 x6 P3
x ld p P7 x1 P0
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x

## Slide 24: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x sub p P6 p P5 x6 P3
x addi P0 x3 P1
x addi P0 x3 P1
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
P8
x x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x
p
p
<x3>
P7

## Slide 25: Repairing Rename at Traps
MIPS R10K rename table is repaired by unrenaming instructions in reverse order using the PRd/LPRd fields
Alpha 21264 had similar physical register file scheme, but kept complete rename table snapshots for each instruction in ROB (80 snapshots total)
  Flash copy all bits from snapshot to active table in one cycle

## Slide 26: Reorder Buffer Holds Active Instructions (Decoded but not Committed)
(Older instructions)
(Newer instructions)
Cycle t
…
ld x1, (x3)
add x3, x1, x2
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x1)
…
Commit
Fetch
Cycle t + 1
Execute
…
ld x1, (x3)
add x3, x1, x2
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x1)
…
ROB contents

## Slide 27: Separate Issue Window from ROB
Reorder buffer used to hold exception information for commit.
The issue window holds only instructions that have been decoded and renamed but not issued into execution. Has register tags and presence bits, and pointer to ROB entry.
op
p1
PR1
p2
PR2
PRd
use
ex
ROB#
ROB is usually several times larger than issue window – why?
Rd
LPRd
PC
Except?
Oldest
Free
Done?

## Slide 28: Superscalar Register Renaming
During decode, instructions allocated new physical destination register
Source operands renamed to physical register with newest value
Execution unit only sees physical register numbers
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Does this work?
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports

## Slide 29: Superscalar Register Renaming
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports
=?
=?
Must check for RAW hazards between instructions issuing in same cycle. Can be done in parallel with rename lookup.
MIPS R10K renames 4 serially-RAW-dependent insts/cycle
Notes: Doesn’t show that update reflects last dest. (jse)

## Slide 30: Load-Store Queue Design
After control hazards (branch prediction in next lecture), data hazards through memory are probably next most important bottleneck to superscalar performance
Modern superscalars use very sophisticated load-store reordering techniques to reduce effective memory latency by allowing loads to be speculatively issued

## Slide 31: Speculative Store Buffer
Just like register updates, stores should not modify the memory until after the instruction is committed. A speculative store buffer is a structure introduced to hold speculative store data.
During decode, store buffer slot allocated in program order
Stores split into “store address” and “store data” micro-operations
“Store address” execution writes tag
“Store data” execution writes data
Store commits when oldest instruction and both address and data available:
  clear speculative bit and eventually move data to cache
On store abort:
  clear valid bit
Data
Tags
Store Commit Path
Speculative Store Buffer
L1 Data Cache
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Store Address
Store Data

## Slide 32: Load bypass from speculative store buffer
If data in both store buffer and cache, which should we use?
  Speculative store buffer
If same address in store buffer twice, which should we use?
  Youngest store older than load
Data
Load Address
Tags
Speculative Store Buffer
L1 Data Cache
Load Data
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V

## Slide 33: Memory Dependencies
sd x1, (x2)
ld x3, (x4)
When can we execute the load?

## Slide 34: In-Order Memory Queue
Execute all loads and stores in program order
=> Load and store cannot leave ROB for execution until all previous loads and stores have completed execution
Can still execute loads and stores speculatively, and out-of-order with respect to other instructions
Need a structure to handle memory ordering…

## Slide 35: Conservative O-o-O Load Execution
sd x1, (x2)
ld x3, (x4)
Can execute load before store, if addresses known and x4 != x2
Each load address compared with addresses of all previous uncommitted stores
  can use partial conservative check i.e., bottom 12 bits of address, to save hardware
Don’t execute load if any previous store address not known
(MIPS R10K, 16-entry address queue)

## Slide 36: Address Speculation
sd x1, (x2)
ld x3, (x4)
Guess that x4 != x2
Execute load before store address known
Need to hold all completed but uncommitted load/store addresses in program order
If subsequently find x4==x2, squash load and all following instructions
=> Large penalty for inaccurate address speculation

## Slide 37: Memory Dependence Prediction (Alpha 21264)
sd x1, (x2)
ld x3, (x4)
Guess that x4 != x2 and execute load before store
If later find x4==x2, squash load and all following instructions, but mark load instruction as store-wait
Subsequent executions of the same load instruction will wait for all previous stores to complete
Periodically clear store-wait bits

## Slide 38: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)