## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 12 – Branch Prediction and Advanced Out-of-Order Superscalars
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 11
Phases of instruction execution:
  Fetch/decode/rename/dispatch/issue/execute/complete/commit
Data-in-ROB design versus unified physical register design
Superscalar register renaming

## Slide 3: Guest Lecturer Today
Following slides are from last year’s lecture

## Slide 4: Control-Flow Penalty
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch
Branch executed
Next fetch started
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution !
How much work is lost if pipeline doesn’t follow correct instruction flow?
~ Loop length x pipeline width + buffers

## Slide 5: Reducing Control-Flow Penalty
Software solutions
  Eliminate branches - loop unrolling
    Increases the run length
  Reduce resolution time - instruction scheduling
    Compute the branch condition as early as possible (of limited value because branches often in critical path through code)
Hardware solutions
  Find something else to do (delay slots)
    Replaces pipeline bubbles with useful work (requires software cooperation) – quickly see diminishing returns
  Speculate, i.e., branch prediction
    Speculative execution of instructions beyond the branch
    Many advances in accuracy, widely used
Notes: Like using compiler to avoid WAW hazards, one can use compiler to reduce control flow penalty.

## Slide 6: Branch Prediction
Motivation:
  Branch penalties limit performance of deeply pipelined processors
  Modern branch predictors have high accuracy
  (>95%) and can reduce branch penalties significantly
Required hardware support:
  Prediction structures:
    Branch history tables, branch target buffers, etc.
  Mispredict recovery mechanisms:
    Keep result computation separate from commit
    Kill instructions following branch in pipeline
    Restore state to that following branch

## Slide 7: Importance of Branch Prediction
Consider 4-way superscalar with 8 pipeline stages from fetch to dispatch, and 80-entry ROB, and 3 cycles from issue to branch resolution
On a mispredict, could throw away 8*4+(80-1)=111 instructions
Improving from 90% to 95% prediction accuracy, removes 50% of branch mispredicts
  If 1/6 instructions are branches, then move from 60 instructions between mispredicts, to 120 instructions between mispredicts

## Slide 8: Static Branch Prediction
Overall probability a branch is taken is ~60-70% but:
ISA can attach preferred direction semantics to branches, e.g., Motorola MC88110
  bne0 (preferred taken) beq0 (not taken)
ISA can allow arbitrary choice of statically predicted direction, e.g., HP PA-RISC, Intel IA-64 typically reported as ~80% accurate
backward
90%
forward
50%

## Slide 9: Dynamic Branch Prediction learning based on past behavior
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)

## Slide 10: One-Bit Branch History Predictor
For each branch, remember last way branch went
Has problem with loop-closing backward branches, as two mispredicts occur on every loop execution
  first iteration predicts loop backwards branch not-taken (loop was exited last time)
  last iteration predicts loop backwards branch taken (loop continued last time)

## Slide 11: Branch Prediction Bits
Assume 2 BP bits per instruction
Change the prediction after two consecutive mistakes!
¬take
wrong
taken
¬ taken
taken
taken
taken
¬take
right
take
right
take
wrong
¬ taken
¬ taken
¬ taken
BP state:
(predict take/¬take) x (last prediction right/wrong)

## Slide 12: Branch History Table (BHT)
4K-entry BHT, 2 bits/entry, ~80-90% correct predictions
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?

## Slide 13: Exploiting Spatial Correlation Yeh and Patt, 1992
History register, H, records the direction of the last N branches executed by the processor
if (x[i] < 7) then
y += 1;
if (x[i] < 5) then
c -= 4;
If first condition false, second condition also false

## Slide 14: Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Taken/¬Taken?

## Slide 15: Speculating Both Directions?
An alternative to branch prediction is to execute both directions of a branch speculatively
  resource requirement is proportional to the number of concurrent speculative executions
  only half the resources engage in useful work when both directions of a branch are executed speculatively
  branch prediction takes less resources than speculative execution of both paths
With accurate branch prediction, it is more cost effective to dedicate all resources to the predicted direction!

## Slide 16: Limitations of BHTs
Only predicts branch direction. Therefore, cannot redirect fetch stream until after branch target is determined.
UltraSPARC-III fetch pipeline
Correctly predicted
taken branch penalty
Jump Register penalty
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
Remainder of execute pipeline
(+ another 6 stages)

## Slide 17: Branch Target Buffer (BTB)
Keep both the branch PC and target PC in the BTB
PC+4 is fetched if match fails
Only taken branches and jumps held in BTB
Next PC determined before branch fetched and decoded
2k-entry direct-mapped BTB
(can also be associative)
I-Cache
PC
k
Valid
valid
Entry PC
=
match
predicted
target
target PC

## Slide 18: Combining BTB and BHT
BTB entries are considerably more expensive than BHT, but can redirect fetches at earlier stage in pipeline and can accelerate indirect branches (JR)
BHT can hold many more entries and is more accurate
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
BTB
BHT
BHT in later pipeline stage corrects when BTB misses a predicted taken branch
BTB/BHT only updated after branch resolves in E stage

## Slide 19: Uses of Jump Register (JR)
Switch statements (jump to address of matching case)
Dynamic function call (jump to run-time function address)
Subroutine returns (jump to return address)
How well does BTB work for each of these cases?
BTB works well if same case used repeatedly
BTB works well if same function usually called, (e.g., in C++ programming, when objects have same type in virtual function call)
BTB works well if usually return to the same place
 Often one function called from many distinct call sites!

## Slide 20: Subroutine Return Stack
Small structure to accelerate JR for subroutine returns, typically much more accurate than BTBs.
&fb()
&fc()
Push call address when function call executed
Pop return address when subroutine return decoded
fa() { fb(); }
fb() { fc(); }
fc() { fd(); }
&fd()
k entries
(typically k=8-16)

## Slide 21: Return Stack in Pipeline
How to use return stack (RS) in deep fetch pipeline?
Only know if subroutine call/return at decode
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
RS
RS Push/Pop after decode gives large bubble in fetch stream.
Return Stack prediction checked

## Slide 22: Return Stack in Pipeline
Can remember whether PC is subroutine call/return using BTB-like structure
Instead of target-PC, just store push/pop bit
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
RS
Push/Pop before instructions decoded!
Return Stack prediction checked

## Slide 23: In-Order vs. Out-of-Order Branch Prediction
Speculative fetch but not speculative execution - branch resolves before later instructions complete
Completed values held in bypass network until commit
Speculative execution, with branches resolved after later instructions complete
Completed values held in rename registers in ROB or unified physical register file until commit
Fetch
Decode
Execute
Commit
In-Order Issue
Out-of-Order Issue
Fetch
Decode
Execute
Commit
ROB
Br. Pred.
Resolve
Br. Pred.
Resolve
Both styles of machine can use same branch predictors in front-end fetch pipeline, and both can execute multiple instructions per cycle
Common to have 10-30 pipeline stages in either style of design
In-Order
In-Order
In-Order
Out-of-Order

## Slide 24: InO vs. OoO Mispredict Recovery
In-order execution?
  Design so no instruction issued after branch can write-back before branch resolves
  Kill all instructions in pipeline behind mispredicted branch
Out-of-order execution?
  Multiple instructions following branch in program order can complete before branch resolves
  A simple solution would be to handle like precise traps
    Problem?

## Slide 25: Branch Misprediction in Pipeline
Can have multiple unresolved branches in ROB
Can resolve branches out-of-order by killing all the instructions in ROB that follow a mispredicted branch
MIPS R10K uses four mask bits to tag instructions that are dependent on up to four speculative branches
Mask bits cleared as branch resolves, and reused for next branch
Fetch
Decode
Execute
Commit
Reorder Buffer
Kill
Kill
Kill
PC
Inject correct PC
Branch
Prediction
Branch
Resolution
Complete

## Slide 26: Rename Table Recovery
Have to quickly recover rename table on branch mispredicts
MIPS R10K only has four snapshots for each of four outstanding speculative branches
Alpha 21264 has 80 snapshots, one per ROB instruction

## Slide 27: CS152 Administrivia
Lab 3 out on Friday, due Monday April 6
PS 3 due Monday March 16

## Slide 28: CS252 Administrivia
Readings next week on OoO superscalar microprocessors
Discussion meeting in SDH 240, Monday 3:30-4:30
  New regular meeting time

## Slide 29: Improving Instruction Fetch
Performance of speculative out-of-order machines often limited by instruction fetch bandwidth
  speculative execution can fetch 2-3x more instructions than are committed
  mispredict penalties dominated by time to refill instruction window
  taken branches are particularly troublesome

## Slide 30: Increasing Taken Branch Bandwidth (Alpha 21264 I-Cache)
Fold 2-way tags and BTB into predicted next block
Take tag checks, inst. decode, branch predict out of loop
Raw RAM speed on critical loop (1 cycle at ~1 GHz)
2-bit hysteresis counter per block prevents overtraining
Cached Instructions
Line Predict
Way Predict
Tag
Way
0
Tag
Way
1
=?
=?
fast fetch path
PC Generation
PC
Branch Prediction
Instruction Decode
Validity Checks
4 insts
Hit/Miss/Way

## Slide 31: Tournament Branch Predictor (Alpha 21264)
Choice predictor learns whether best to use local or global branch history in predicting next branch
Global history is speculatively updated but restored on mispredict
Claim 90-100% success on range of applications
Local history table (1,024x10b)
PC
Local prediction (1,024x3b)
Global Prediction (4,096x2b)
Choice Prediction (4,096x2b)
Global History (12b)
Prediction

## Slide 32: Taken Branch Limit
Integer codes have a taken branch every 6-9 instructions
To avoid fetch bottleneck, must execute multiple taken branches per cycle when increasing performance
This implies:
  predicting multiple branches per cycle
  fetching multiple non-contiguous blocks per cycle

## Slide 33: Branch Address Cache (Yeh, Marr, Patt)
PC
k
Entry PC
=
match
Valid
valid
predicted
target#1
target #1
len
len#1
predicted
target#2
target #2
Extend BTB to return multiple branch predictions per cycle

## Slide 34: Fetching Multiple Basic Blocks
Requires either
  multiported cache: expensive
  interleaving: bank conflicts will occur
Merging multiple blocks to feed to decoders adds latency, increasing mispredict penalty and reducing branch throughput

## Slide 35: Trace Cache
Key Idea: Pack multiple non-contiguous basic blocks into one contiguous trace cache line
BR
BR
BR
Single fetch brings in multiple basic blocks
Trace cache indexed by start address and next n branch predictions
Used in Intel Pentium-4 processor to hold decoded uops
BR
BR
BR

## Slide 36: Load-Store Queue Design
After control hazards, data hazards through memory are probably next most important bottleneck to superscalar performance
Modern superscalars use very sophisticated load-store reordering techniques to reduce effective memory latency by allowing loads to be speculatively issued

## Slide 37: Speculative Store Buffer
Just like register updates, stores should not modify the memory until after the instruction is committed. A speculative store buffer is a structure introduced to hold speculative store data.
During decode, store buffer slot allocated in program order
Stores split into “store address” and “store data” micro-operations
“Store address” execution writes tag
“Store data” execution writes data
Store commits when oldest instruction and both address and data available:
  clear speculative bit and eventually move data to cache
On store abort:
  clear valid bit
Data
Tags
Store Commit Path
Speculative Store Buffer
L1 Data Cache
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Store Address
Store Data

## Slide 38: Load bypass from speculative store buffer
If data in both store buffer and cache, which should we use?
  Speculative store buffer
If same address in store buffer twice, which should we use?
  Youngest store older than load
Data
Load Address
Tags
Speculative Store Buffer
L1 Data Cache
Load Data
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V

## Slide 39: Memory Dependencies
sd x1, (x2)
ld x3, (x4)
When can we execute the load?

## Slide 40: In-Order Memory Queue
Execute all loads and stores in program order
=> Load and store cannot leave ROB for execution until all previous loads and stores have completed execution
Can still execute loads and stores speculatively, and out-of-order with respect to other instructions
Need a structure to handle memory ordering…

## Slide 41: Conservative O-o-O Load Execution
sd x1, (x2)
ld x3, (x4)
Can execute load before store, if addresses known and x4 != x2
Each load address compared with addresses of all previous uncommitted stores
  can use partial conservative check i.e., bottom 12 bits of address, to save hardware
Don’t execute load if any previous store address not known
(MIPS R10K, 16-entry address queue)

## Slide 42: Address Speculation
sd x1, (x2)
ld x3, (x4)
Guess that x4 != x2
Execute load before store address known
Need to hold all completed but uncommitted load/store addresses in program order
If subsequently find x4==x2, squash load and all following instructions
=> Large penalty for inaccurate address speculation

## Slide 43: Memory Dependence Prediction (Alpha 21264)
sd x1, (x2)
ld x3, (x4)
Guess that x4 != x2 and execute load before store
If later find x4==x2, squash load and all following instructions, but mark load instruction as store-wait
Subsequent executions of the same load instruction will wait for all previous stores to complete
Periodically clear store-wait bits

## Slide 44: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)