## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 13 –VLIW
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 12
Branch prediction
  temporal, history of a single branch
  spatial, based on path through multiple branches
Branch History Table (BHT) vs. Branch History Buffer (BTB)
  tradeoff in capacity versus latency
Return-Address Stack (RAS)
  specialized structure to predict subroutine return addresses
Advanced branch prediction structures
  Perceptron
  TAGE

## Slide 3: Superscalar Control Logic Scaling
Each issued instruction must somehow check against W*L instructions, i.e., growth in hardware  W*(W*L)
For in-order machines, L is related to pipeline latencies and check is done during issue (interlocks or scoreboard)
For out-of-order machines, L also includes time spent in instruction buffers (instruction window or ROB), and check is done by broadcasting tags to waiting instructions at write back (completion)
As W increases, larger instruction window is needed to find enough parallelism to keep machine busy => greater L
=> Out-of-order control logic grows faster than W2 (~W3)
Lifetime L
Issue Group
Previously Issued Instructions
Issue Width W

## Slide 4: Out-of-Order Control Complexity: MIPS R10000
Control Logic
[ SGI/MIPS Technologies Inc., 1995 ]

## Slide 5: Sequential ISA Bottleneck
Check instruction dependencies
Superscalar processor
a = foo(b);
for (i=0, i<
Sequential source code
Superscalar compiler
Find independent operations
Schedule operations
Sequential machine code
Schedule execution

## Slide 6: VLIW: Very Long Instruction Word
Multiple operations packed into one instruction
Each operation slot is for a fixed function
Constant operation latencies are specified
Architecture requires guarantee of:
  Parallelism within an instruction => no cross-operation RAW check
  No data use before data ready => no data interlocks
Two Integer Units,
Single-Cycle Latency
Two Load/Store Units,
Three-Cycle Latency
Two Floating-Point Units,
Four-Cycle Latency
Int Op 2
Mem Op 1
Mem Op 2
FP Op 1
FP Op 2
Int Op 1

## Slide 7: Early VLIW Machines
FPS AP120B (1976)
  scientific attached array processor
  first commercial wide instruction machine
  hand-coded vector math libraries using software pipelining and loop unrolling
Multiflow Trace (1987)
  commercialization of ideas from Fisher’s Yale group including “trace scheduling”
  available in configurations with 7, 14, or 28 operations/instruction
  28 operations packed into a 1024-bit instruction word
Cydrome Cydra-5 (1987)
  7 operations encoded in 256-bit instruction word
  rotating register file

## Slide 8: VLIW Compiler Responsibilities
Schedule operations to maximize parallel execution
Guarantees intra-instruction parallelism
Schedule to avoid data hazards (no interlocks)
  Typically separates operations with explicit NOPs

## Slide 9: Loop Execution
How many FP ops/cycle?
for (i=0; i<N; i++)
B[i] = A[i] + C;
Int1
Int 2
M1
M2
FP+
FPx
loop:
fld
add x1
fadd
fsd
add x2
bne
1 fadd / 8 cycles = 0.125
loop: fld f1, 0(x1)
add x1, 8
fadd f2, f0, f1
fsd f2, 0(x2)
add x2, 8
bne x1, x3, loop
Compile
Schedule

## Slide 10: Loop Unrolling
for (i=0; i<N; i++)
B[i] = A[i] + C;
for (i=0; i<N; i+=4)
{
B[i] = A[i] + C;
B[i+1] = A[i+1] + C;
B[i+2] = A[i+2] + C;
B[i+3] = A[i+3] + C;
}
Unroll inner loop to perform 4 iterations at once
Need to handle values of N that are not multiples of unrolling factor with final cleanup loop

## Slide 11: Scheduling Loop Unrolled Code
loop: fld f1, 0(x1)
fld f2, 8(x1)
fld f3, 16(x1)
fld f4, 24(x1)
add x1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
fsd f5, 0(x2)
fsd f6, 8(x2)
fsd f7, 16(x2)
fsd f8, 24(x2)
add x2, 32
bne x1, x3, loop
Schedule
Int1
Int 2
M1
M2
FP+
FPx
loop:
Unroll 4 ways
fld f1
fld f2
fld f3
fld f4
add x1
fadd f5
fadd f6
fadd f7
fadd f8
fsd f5
fsd f6
fsd f7
fsd f8
add x2
bne
How many FLOPS/cycle?
4 fadds / 11 cycles = 0.36

## Slide 12: Software Pipelining
How many FLOPS/cycle?
loop: fld f1, 0(x1)
fld f2, 8(x1)
fld f3, 16(x1)
fld f4, 24(x1)
add x1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
fsd f5, 0(x2)
fsd f6, 8(x2)
fsd f7, 16(x2)
add x2, 32
fsd f8, -8(x2)
bne x1, x3, loop
Int1
Int 2
M1
M2
FP+
FPx
Unroll 4 ways first
fld f1
fld f2
fld f3
fld f4
fadd f5
fadd f6
fadd f7
fadd f8
fsd f5
fsd f6
fsd f7
fsd f8
add x1
add x2
bne
fld f1
fld f2
fld f3
fld f4
fadd f5
fadd f6
fadd f7
fadd f8
fsd f5
fsd f6
fsd f7
fsd f8
add x1
add x2
bne
fld f1
fld f2
fld f3
fld f4
fadd f5
fadd f6
fadd f7
fadd f8
fsd f5
add x1
loop:
iterate
prolog
epilog
4 fadds / 4 cycles = 1

## Slide 13: Software Pipelining vs. Loop Unrolling
time
performance
time
performance
Loop Unrolled
Software Pipelined
Startup overhead
Wind-down overhead
Loop Iteration
Loop Iteration
Software pipelining pays startup/wind-down costs only once per loop, not once per iteration

## Slide 14: CS152 Administrivia
Lab 3 out today, due Monday April 5 (after spring break)
PS 3 due Monday March 15
Midterm regrade requests due in one week
  Tuesday March 16 11:59PM

## Slide 15: CS152 Midterm 1 Stats

## Slide 16: CS252 Administrivia
Second half of project presentations this week
Readings next week on OoO superscalar microprocessors

## Slide 17: What if there are no loops?
Branches limit basic block size in control-flow intensive irregular code
Difficult to find ILP in individual basic blocks
Basic block

## Slide 18: Trace Scheduling [ Fisher,Ellis]
Pick string of basic blocks, a trace, that represents most frequent branch path
Use profiling feedback or compiler heuristics to find common branch paths
Schedule whole “trace” at once
Add fixup code to cope with branches jumping out of trace

## Slide 19: Problems with “Classic” VLIW
Object-code compatibility
  have to recompile all code for every machine, even for two machines in same generation
Object code size
  instruction padding wastes instruction memory/cache
  loop unrolling/software pipelining replicates code
Scheduling variable latency memory operations
  caches and/or memory bank conflicts impose statically unpredictable variability
Knowing branch probabilities
  Profiling requires an significant extra step in build process
Scheduling for statically unpredictable branches
  optimal schedule varies with branch path

## Slide 20: VLIW Instruction Encoding
Schemes to reduce effect of unused fields
  Compressed format in memory, expand on I-cache refill
    used in Multiflow Trace
    introduces instruction addressing challenge
  Mark parallel groups
    used in TMS320C6x DSPs, Intel IA-64
  Provide a single-op VLIW instruction
    Cydra-5 UniOp instructions
Group 1
Group 2
Group 3

## Slide 21: Intel Itanium, EPIC IA-64
EPIC is the style of architecture (cf. CISC, RISC)
  Explicitly Parallel Instruction Computing (really just VLIW)
IA-64 is Intel’s chosen ISA (cf. x86, MIPS)
  IA-64 = Intel Architecture 64-bit
  An object-code-compatible VLIW
Merced was first Itanium implementation (cf. 8086)
  First customer shipment expected 1997 (actually 2001)
  McKinley, second implementation shipped in 2002
  Recent version, Poulson, eight cores, 32nm, announced 2011

## Slide 22: Eight Core Itanium “Poulson” [Intel 2011]
8 cores
1-cycle 16KB L1 I&D caches
9-cycle 512KB L2 I-cache
8-cycle 256KB L2 D-cache
32 MB shared L3 cache
544mm2 in 32nm CMOS
Over 3 billion transistors
Cores are 2-way multithreaded
6 instruction/cycle fetch
  Two 128-bit bundles
Up to 12 insts/cycle execute

## Slide 23: IA-64 Instruction Format
Template bits describe grouping of these instructions with others in adjacent bundles
Each group contains instructions that can execute in parallel
Instruction 2
Instruction 1
Instruction 0
Template
128-bit instruction bundle
group i
group i+1
group i+2
group i-1
bundle j
bundle j+1
bundle j+2
bundle j-1

## Slide 24: IA-64 Registers
128 General Purpose 64-bit Integer Registers
128 General Purpose 64/80-bit Floating Point Registers
64 1-bit Predicate Registers
GPRs “rotate” to reduce code size for software pipelined loops
  Rotation is a simple form of register renaming allowing one instruction to address different physical registers on each iteration

## Slide 25: Rotating Register Files
Problems: Scheduled loops require lots of registers, Lots of duplicated code in prolog, epilog
Solution: Allocate new set of registers for each loop iteration
25

## Slide 26: Rotating Register File
P0
P1
P2
P3
P4
P5
P6
P7
RRB=3
+
R1
Rotating Register Base (RRB) register points to base of current register set. Value added on to logical register specifier to give physical register number. Usually, split into rotating and non-rotating registers.
26

## Slide 27: Rotating Register File (Previous Loop Example)
bloop
sd f9, ()
fadd f5, f4, ...
ld f1, ()
Three cycle load latency encoded as difference of 3 in register specifier number (f4 - f1 = 3)
Four cycle fadd latency encoded as difference of 4 in register specifier number (f9 – f5 = 4)
bloop
sd P17, ()
fadd P13, P12,
ld P9, ()
RRB=8
bloop
sd P16, ()
fadd P12, P11,
ld P8, ()
RRB=7
bloop
sd P15, ()
fadd P11, P10,
ld P7, ()
RRB=6
bloop
sd P14, ()
fadd P10, P9,
ld P6, ()
RRB=5
bloop
sd P13, ()
fadd P9, P8,
ld P5, ()
RRB=4
bloop
sd P12, ()
fadd P8, P7,
ld P4, ()
RRB=3
bloop
sd P11, ()
fadd P7, P6,
ld P3, ()
RRB=2
bloop
sd P10, ()
fadd P6, P5,
ld P2, ()
RRB=1
27

## Slide 28: IA-64 Predicated Execution
Problem: Mispredicted branches limit ILP
Solution: Eliminate hard to predict branches with predicated execution
  Almost all IA-64 instructions can be executed conditionally under predicate
  Instruction becomes NOP if predicate register false
Inst 1
Inst 2
br a==b, b2
Inst 3
Inst 4
br b3
Inst 5
Inst 6
Inst 7
Inst 8
b0:
b1:
b2:
b3:
if
else
then
Four basic blocks
Inst 1
Inst 2
p1,p2 <- cmp(a==b)
(p1) Inst 3 || (p2) Inst 5
(p1) Inst 4 || (p2) Inst 6
Inst 7
Inst 8
Predication
One basic block
Mahlke et al, ISCA95: On average >50% branches removed
Warning: Complicates bypassing!

## Slide 29: IA-64 Speculative Execution
Problem: Branches restrict compiler code motion
Inst 1
Inst 2
br a==b, b2
Load r1
Use r1
Inst 3
Can’t move load above branch because might cause spurious exception
Load.s r1
Inst 1
Inst 2
br a==b, b2
Chk.s r1
Use r1
Inst 3
Speculative load never causes exception, but sets “poison” bit on destination register
Check for exception in original home block jumps to fixup code if exception detected
Particularly useful for scheduling long latency loads early
Solution: Speculative operations that don’t cause exceptions

## Slide 30: IA-64 Data Speculation
Problem: Possible memory hazards limit code scheduling
Requires associative hardware in address check table
Inst 1
Inst 2
Store
Load r1
Use r1
Inst 3
Can’t move load above store because store might be to same address
Load.a r1
Inst 1
Inst 2
Store
Load.c
Use r1
Inst 3
Data speculative load adds address to address check table
Store invalidates any matching loads in address check table
Check if load invalid (or missing), jump to fixup code if so
Solution: Hardware to check pointer hazards

## Slide 31: Limits of Static Scheduling
Statically unpredictable branches
Variable memory latency (unpredictable cache misses)
Code size explosion
Compiler complexity
Despite several attempts, VLIW has failed in general-purpose computing arena (so far).
  More complex VLIW architectures are close to in-order superscalar in complexity, no real advantage on large complex apps.
Successful in embedded DSP market
  Simpler VLIWs with more constrained environment, friendlier code.

## Slide 32: Intel Kills Itanium
Donald Knuth “ … Itanium approach that was supposed to be so terrific—until it turned out that the wished-for compilers were basically impossible to write.”
“Intel officially announced the end of life and product discontinuance of the Itanium CPU family on January 30th, 2019”, Wikipedia

## Slide 33: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)