## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 15 – Vectors
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time Lecture 14: Multithreading
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 3: Supercomputer Applications
Typical application areas
  Military research (nuclear weapons, cryptography)
  Scientific research
  Weather forecasting
  Oil exploration
  Industrial design (car crash simulation)
  Bioinformatics
  Cryptography
All involve huge computations on large data set
Supercomputers: CDC6600, CDC7600, Cray-1, …
In 70s-80s, Supercomputer  Vector Machine

## Slide 4: Vector Supercomputers
Epitomized by Cray-1, 1976:
Scalar Unit
  Load/Store Architecture
Vector Extension
  Vector Registers
  Vector Instructions
Implementation
  Hardwired Control
  Highly Pipelined Functional Units
  Interleaved Memory System
  No Data Caches
  No Virtual Memory
[©Cray Research, 1976]

## Slide 5: Vector Programming Model
+
+
+
+
+
+
[0]
[1]
[vl-1]
Vector Arithmetic Instructions
vadd v3,v1,v2
v3
v2
v1
Scalar Registers
x0
x31
Vector Registers
v0
v31
[0]
[1]
[2]
[VLMAX-1]
vl
Vector Length Register
v1
Vector Load and Store Instructions
vls v1,(x1),x2
Base, x1
Stride, x2
Memory
Vector Register

## Slide 6: Vector Code Example
# Scalar Code
li x4, 64
loop:
fld f1, 0(x1)
fld f2, 0(x2)
fadd.d f3,f1,f2
fsd f3, 0(x3)
addi x1, x1, 8
addi x2, x2, 8
addi x3, x3, 8
subi x4, x4, 1
bnez x4, loop
# Vector Code
li x4, 64
vsetvl x4
vld v1, (x1)
vld v2, (x2)
vadd v3,v1,v2
vst v3, (x3)
# C code
for (i=0; i<64; i++)
C[i] = A[i] + B[i];

## Slide 7: Cray-1 (1976)
Single-Port
Memory
16 banks of 64-bit words
+
8-bit SECDED
80MW/sec data load/store
320MW/sec instruction
buffer refill
4 Instruction Buffers
64-bitx16
NIP
LIP
CIP
(A0)
( (Ah) + j k m )
64
T Regs
(A0)
( (Ah) + j k m )
64
B Regs
S0
S1
S2
S3
S4
S5
S6
S7
A0
A1
A2
A3
A4
A5
A6
A7
Si
Tjk
Ai
Bjk
FP Add
FP Mul
FP Recip
Int Add
Int Logic
Int Shift
Pop Cnt
Sj
Si
Sk
Addr Add
Addr Mul
Aj
Ai
Ak
memory bank cycle 50 ns processor cycle 12.5 ns (80MHz)
V0
V1
V2
V3
V4
V5
V6
V7
Vk
Vj
Vi
V. Mask
V. Length
64 Element Vector Registers

## Slide 8: Vector Instruction Set Advantages
Compact
  one short instruction encodes N operations
Expressive, tells hardware that these N operations:
  are independent
  use the same functional unit
  access disjoint registers
  access registers in same pattern as previous instructions
  access a contiguous block of memory (unit-stride load/store)
  access memory in a known pattern (strided load/store)
Scalable
  can run same code on more parallel pipelines (lanes)

## Slide 9: Vector Arithmetic Execution
Use deep pipeline (=> fast clock) to execute element operations
Simplifies control of deep pipeline because elements in vector are independent (=> no hazards!)
v1
v2
v3
v3 <- v1 * v2
Six-stage multiply pipeline

## Slide 10: Vector Instruction Execution
vadd vc, va, vb
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units

## Slide 11: Interleaved Vector Memory System
Bank busy time: Time before bank ready to accept next request
Cray-1, 16 banks, 4 cycle bank busy time, 12 cycle latency
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator

## Slide 12: Vector Unit Structure
Lane
Functional Unit
Vector
Registers
Memory Subsystem
Elements 0, 4, 8, …
Elements 1, 5, 9, …
Elements 2, 6, 10, …
Elements 3, 7, 11, …

## Slide 13: T0 Vector Microprocessor (UCB/ICSI, 1995)
Lane
Vector register elements striped over lanes
[0]
[8]
[16]
[24]
[1]
[9]
[17]
[25]
[2]
[10]
[18]
[26]
[3]
[11]
[19]
[27]
[4]
[12]
[20]
[28]
[5]
[13]
[21]
[29]
[6]
[14]
[22]
[30]
[7]
[15]
[23]
[31]

## Slide 14: Vector Instruction Parallelism
Can overlap execution of multiple vector instructions
  example machine has 32 elements per vector register and 8 lanes
load
load
mul
mul
add
add
Load Unit
Multiply Unit
Add Unit
time
Instruction issue
Complete 24 operations/cycle while issuing 1 short instruction/cycle

## Slide 15: Vector Chaining
Vector version of register bypassing
  introduced with Cray-1
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
vld v1
vmul v3,v1,v2
vadd v5, v3,v4

## Slide 16: Vector Chaining Advantage
With chaining, can start dependent instruction as soon as first result appears
Load
Mul
Add
Load
Mul
Add
Time
Without chaining, must wait for last element of result to be written before starting dependent instruction

## Slide 17: Vector Startup
Two components of vector startup penalty
  functional unit latency (time through pipeline)
  dead time or recovery time (time before another vector instruction can start down pipeline)
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
Functional Unit Latency
Dead Time
First Vector Instruction
Second Vector Instruction
Dead Time

## Slide 18: Dead Time and Short Vectors
Cray C90, Two lanes
4-cycle dead time
Maximum efficiency 94% with 128-element vectors
4 cycles dead time
T0, Eight lanes
No dead time
100% efficiency with 8-element vectors
No dead time
64 cycles active

## Slide 19: Vector Memory-Memory versus Vector Register Machines
Vector memory-memory instructions hold all vector operands in main memory
The first vector machines, CDC Star-100 (‘73) and TI ASC (‘71), were memory-memory machines
Cray-1 (’76) was first vector register machine
for (i=0; i<N; i++)
{
C[i] = A[i] + B[i];
D[i] = A[i] - B[i];
}
Example Source Code
vadd (C),(A),(B)
vsub (D),(A),(B)
Vector Memory-Memory Code
vld V1, (A)
vld V2, (B)
vadd V3, V1, V2
vst V3, (C)
vsub V4, V1, V2
vst V4, (D)
Vector Register Code

## Slide 20: Vector Memory-Memory vs. Vector Register Machines
Vector memory-memory architectures (VMMA) require greater main memory bandwidth, why?
  All operands must be read in and out of memory
VMMAs make if difficult to overlap execution of multiple vector operations, why?
  Must check dependencies on memory addresses
VMMAs incur greater startup latency
  Scalar code was faster on CDC Star-100 for vectors < 100 elements
  For Cray-1, vector/scalar breakeven point was around 2-4 elements
Apart from CDC follow-ons (Cyber-205, ETA-10) all major vector machines since Cray-1 have had vector register architectures
(we ignore vector memory-memory from now on)

## Slide 21: CS152 Administrivia
PS 4 out today, due Monday April 5
Lab 3 due Monday April 5
No lectures or sections next week!
  Spring Break (March 22-26)

## Slide 22: CS252 Administrivia
Readings on OoO architectures this Thursday

## Slide 23: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vectorization is a massive compile-time reordering of operation sequencing
requires extensive loop-dependence analysis
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time

## Slide 24: Vector Stripmining
Problem: Vector registers have finite length
Solution: Break loops into pieces that fit in registers, “Stripmining”
andi x1, xN, 63 # N mod 64
vsetvl x1 # Do remainder
loop:
vld v1, (xA)
slli x2, x1, 3 # Multiply by 8
add xA, xA, x2 # Bump pointer
vld v2, (xB)
add xB, xB, x2
vadd v3, v1, v2
vst v3, (xC)
add xC, xC, x2
sub xN, xN, x1 # Subtract elements
li x1, 64
vsetvl x1 # Reset full length
bgtz xN, loop # Any more to do?
for (i=0; i<N; i++)
C[i] = A[i]+B[i];
+
+
+
A
B
C
64 elements
Remainder

## Slide 25: Vector Conditional Execution
Problem: Want to vectorize loops with conditional code:
      for (i=0; i<N; i++)
      if (A[i]>0) then
      A[i] = B[i];
Solution: Add vector mask (or flag) registers
  vector version of predicate registers, 1 bit per element
…and maskable vector instructions
  vector operation becomes bubble (“NOP”) at elements where mask bit is clear
Code example:
  cvm # Turn on all elements
  vld vA, (xA) # Load entire A vector
  vgt vA, f0 # Set bits in mask register where A>0
  vld vA, (xB) # Load B vector into A under mask
  vst vA, (xA) # Store A back to memory under mask

## Slide 26: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
Write data port
Write Enable
A[7]
B[7]
M[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask

## Slide 27: Compress/Expand Operations
Compress packs non-masked elements from one vector register contiguously at start of destination vector register
  population count of mask vector gives packed vector length
Expand performs inverse operation
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
A[3]
A[4]
A[5]
A[6]
A[7]
A[0]
A[1]
A[2]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
B[3]
A[4]
A[5]
B[6]
A[7]
B[0]
A[1]
B[2]
Expand
A[7]
A[1]
A[4]
A[5]
Compress
A[7]
A[1]
A[4]
A[5]
Used for density-time conditionals and also for general selection operations

## Slide 28: Vector Reductions
Problem: Loop-carried dependence on reduction variables
  sum = 0;
  for (i=0; i<N; i++)
  sum += A[i]; # Loop-carried dependence on sum
Solution: Re-associate operations if possible, use binary tree to perform reduction
  # Rearrange as:
  sum[0:VL-1] = 0 # Vector of VL partial sums
  for(i=0; i<N; i+=VL) # Stripmine VL-sized chunks
  sum[0:VL-1] += A[i:i+VL-1]; # Vector sum
  # Now have VL partial sums in one vector register
  do {
  VL = VL/2; # Halve vector length
  sum[0:VL-1] += sum[VL:2*VL-1] # Halve no. partials
  } while (VL>1)

## Slide 29: Vector Scatter/Gather
Want to vectorize loops with indirect accesses:
  for (i=0; i<N; i++)
  A[i] = B[i] + C[D[i]]
Indexed load instruction (Gather)
  vld vD, (xD) # Load indices in D vector
  vlx vC, (xC), vD # Load indexed from xC base
  vld vB, (xB) # Load B vector
  vadd vA,vB,vC # Do add
  vst vA, (xA) # Store result

## Slide 30: Histogram with Scatter/Gather
Histogram example:
  for (i=0; i<N; i++)
  A[B[i]]++;
Is following a correct translation?
  vld vB, (xB) # Load indices in B vector
  vlx vA, (xA), vB # Gather initial A values
  vadd vA, vA, 1 # Increment
  vsx vA, (xA), vB # Scatter incremented values

## Slide 31: Vector Memory Models
Some vector machines have a very relaxed memory model, e.g.
  vst v1, (x1) # Store vector to x1
  vld v2, (x1) # Load vector from x1
  No guarantee that elements of v2 will have value of elements of v1 even when store and load execute by same processor!
So require explicit memory barrier or fence
  vst v1, (x1) # Store vector to x1
  fence # Enforce ordering s->l
  vld v2, (x1) # Load vector from x1
Vector machines support highly parallel memory systems (multiple lanes and multiple load and store units) with long latency (100+ clock cycles)
  hardware coherence checks would be prohibitively expensive
  vectorizing compiler can eliminate most dependencies

## Slide 32: Packed SIMD Extensions
Very short vectors added to existing ISAs for microprocessors
Use existing 64-bit registers split into 2x32b or 4x16b or 8x8b
  Lincoln Labs TX-2 from 1957 had 36b datapath split into 2x18b or 4x9b
  Newer designs have wider registers
    128b for PowerPC Altivec, Intel SSE2/3/4
    256b/512b for Intel AVX
Single instruction operates on all elements within register
16b
16b
16b
16b
32b
32b
64b
8b
8b
8b
8b
8b
8b
8b
8b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
+
+
+
+
4x16b adds

## Slide 33: Packed SIMD versus Vectors
Limited instruction set:
  no vector length control
  no strided load/store or scatter/gather
  unit-stride loads must be aligned to 64/128-bit boundary
Limited vector register length:
  requires superscalar dispatch to keep multiply/add/load units busy
  loop unrolling to hide latencies increases register pressure
Trend towards fuller vector support in microprocessors
  Better support for misaligned memory accesses
  Support of double-precision (64-bit floating-point)
  New Intel AVX spec (announced April 2008), 256b vector registers (expandable up to 1024b), gather added, scatter to follow
  ARM Scalable Vector Extensions (SVE)

## Slide 34: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)