## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 17 – RISC-V Vectors
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152
Released Under Creative Commons CC BY-SA 4.0 Licence (see last slide)

## Slide 2: Last Time in Lecture 16
GPU architecture
Evolved from graphics-only, to more general-purpose computing
GPUs programmed as attached accelerators, with software required to separate GPU from CPU code, move memory
Many cores, each with many lanes
  thousands of lanes on current high-end GPUs
SIMT model has hardware management of conditional execution
  code written as scalar code with branches, executed as vector code with predication

## Slide 3: New RISC-V “V” Vector Extension
Being added as a standard extension to the RISC-V ISA
  An updated form of Cray-style vectors for modern microprocessors
  Appearing in commercial implementations from Alibaba, Andes, Semidynamics, SiFive, …
  Basis of European supercomputer initiative (EPI)
Today, a short tutorial on current draft standard, v0.10
  v0.10 is intended to be close to final version of RISC-V vector extension
  Still a work in progress, so details might change before standardization
  https://github.com/riscv/riscv-v-spec

## Slide 4: RISC-V Scalar State
Program counter (pc)
32x32/64-bit integer registers (x0-x31)
x0 always contains a 0
Floating-point (FP), adds 32 registers (f0-f31)
each can contain a single- or double-precision FP value (32-bit or 64-bit IEEE FP)
FP status register (fcsr), used for FP rounding mode & exception reporting
ISA string options:
RV32I (XLEN=32, no FP)
RV32IF (XLEN=32, FLEN=32)
RV32ID (XLEN=32, FLEN=64)
RV64I (XLEN=64, no FP)
RV64IF (XLEN=64, FLEN=32)
RV64ID (XLEN=64, FLEN=64)

## Slide 5: Vector Extension Additional State
32 vector data registers, v0-v31, each VLEN bits long
Vector length register vl
Vector type register vtype
Other control registers:
  vstart
    For trap handling
  vrm/vxsat
    Fixed-point rounding mode/saturation
    Also appear in separate vcsr
  vlenb
    Gives vector length in bytes (read-only)
v31
vl
vtype
Vector length register
Vector data registers
VLEN bits per vector register, (implementation-dependent)
v0
Vector type register

## Slide 6: Vector Type Register (vtype)
vsew[2:0] field encodes standard element width (SEW) in bits of elements in vector register (SEW = 8*2vsew )
vlmul[2:0] encodes vector register length multiplier (LMUL = 2vlmul = 1/8 - 8)
Ideally, info would be in instruction encoding, but no space in 32-bit instructions.
Planned 64-bit encoding extension would add these as instruction bits.
vta specifies tail-agnostic
vma specifies mask-agnostic

## Slide 7: Example Vector Register Data Layouts (LMUL=1)

## Slide 8: Setting vector configuration, vsetvli/vsetivli/vsetvl
vsetvli rd, rs1, e8 # Set SEW=8, vl=min(VLEN/SEW,rs1), rd=vl
Requested application vector length
Resulting machine vector length setting
vtype parameters (SEW,LMUL,TA,MA) encoded as immediate in instruction
The vset{i}vl{i} configuration instructions set the vtype register, and also set the vl register, returning the vl value in a scalar register
Usually use register-immediate form, vsetvli, to set vtype parameters.
Immediate-immediate form, vsetivli, used when vector length known statically
The register-register version vsetvl is usually used only for context save/restore
Instruction encoding

## Slide 9: Vset{i}vl{i} operation
The first argument, rs1 or 5-bit immediate, is the requested application vector length (AVL)
The type argument (either 10/11-bit immediate or second register rs2) indicates how the vector registers should be configured
  Configuration includes size of each element, SEW, and LMUL value
The vector length is set to the minimum of requested AVL and the maximum supported vector length (VLMAX) in the new configuration
  VLMAX = LMUL*VLEN/SEW
  vl = min(AVL, VLMAX)
The value placed in vl is also written to the scalar destination register rd

## Slide 10: Simple stripmined vector memcpy example
Unit-stride vector load elements (bytes)
Unit-stride vector store elements (bytes)
Set configuration, calculate vector strip length
Same binary machine code can run on machines with any VLEN!

## Slide 11: Vector Load and Store Instructions

## Slide 12: Vector Unit-Stride Loads/Stores

## Slide 13: Vector Strided Load/Store Instructions

## Slide 14: Vector Indexed Loads/Stores
Index data width encoded in instruction, while data size encoded in vtype.vsew field

## Slide 15: Vector Length Multiplier, LMUL
Set by vlmul[2:0] field in vtype during setvli
Gives fewer but longer vector registers
  Called “vector register groups” – operate as single vectors
  Must use even register names only for LMUL=2 (v0,v2,..), and every fourth register for LMUL=4 (v0,v4, …), etc.
Used for 1) accommodate mixed-width operations, and/or 2) to increase efficiency by using longer vectors when fewer separate registers needed

## Slide 16: LMUL=8 stripmined vector memcpy example
Unit-stride vector load bytes
Unit-stride vector store bytes
Set configuration, calculate vector strip length
Binary machine code can run on machines with any VLEN!
Combine eight vector registers into group
(v0,v1,…,v7)

## Slide 17: Vector Integer Add Instructions

## Slide 18: Vector FP Add Instructions
SEW can be 16b, 32b, 64b, 128b for half/single/double/quad FP
Scalar values come from floating-point f registers

## Slide 19: CS152 Administrivia
PS 4 and Lab 3 due Monday April 5
Lab 4 out today!
Special Announcement, Project Prizes!
  Apple donating specially engraved Airpod Pro as prizes
  Awarded to top two teams in open-ended portions of labs 3,4,5

## Slide 20: CS252 Administrivia
This week’s readings: Branch Prediction
Project prize, sponsored by Apple
  Top team receives engraved Airpod Pros

## Slide 21: Masking
Nearly all operations can be optionally under a mask (or predicate) held in vector register v0
A single vm bit in instruction encoding selects whether unmasked or under control of v0
Constrained by encoding space in 32-bit instructions
  Longer 64-bit encoding extension will support predicate in any register
Integer and FP compare instructions provided to set masks into any vector register
Can perform mask logical operations between any vector registers

## Slide 22: Integer Compare Instructions

## Slide 23: Mask Logical Operations

## Slide 24: Prestart, Active, Inactive, Body, and Tail Elements

## Slide 25: Vector Arithmetic Instruction Encodings

## Slide 26: Widening Integer Add Instructions

## Slide 27: Widening FP Mul-Add

## Slide 28: Mixed-Width Loops
Have different element widths in one loop, even in one instruction
  e.g., widening multiply, 16b*16b -> 32b product
Want same number of elements in each vector register, even if different bits/element
Solution: Keep SEW/LMUL constant

## Slide 29
VLEN=128b
VLMAX=16
VLMAX=16
VLMAX=16
VLMAX=16
SEW/LMUL=8

## Slide 30: Mask Register Layout
Masks always held in a single vector register (no groups)
  Single bit per mask element, stored packed
  With maximum LMUL=8 and minimum SEW=8, all bits of vector register used

## Slide 31: SAXPY Example

## Slide 32: Conditional/Mixed Width Example

## Slide 33: Creative Commons Licence
These lecture slides are made available under a CC SY-BA 4.0 license
https://creativecommons.org/licenses/by-sa/4.0/
Attribution Title: “RISC-V Vectors, CS152, Spring 2021”
Attribution Author: Krste Asanovic
Original content link: http://inst.eecs.berkeley.edu/~cs152/sp21/lectures/L17-RISCV-Vectors.pptx